ATMakers
SwitchBoard
Relay
FeatherWing
User's Guide

For Board Rev A (1.0) and B

DRAFT 2018-09-20

# Introduction
The ATMakers' SwitchBoard is a set of five relays and a current sensor arranged on a FeatherWing form factor PC board. An attached Feather micro-controller can control each of the five relays independently and read the current flowing through the current sensor terminals. A GPIO Expander facilitates the control of the relays via the I2C bus, thus freeing up any I/O pins that would be used otherwise.
The relays are double-pole, double-throw latching relays. Relay and current sensor I/O is available via solder terminals at the sides of the board where screw terminals, headers, or point-to-point wiring can be soldered.
Up to four SwitchBoards can be addressed on one I2C bus thereby allowing one Feather to control up to twenty DPDT latching relays.
The SwitchBoard concept was proposed by Bill Binko of ATMakers.org.
# Applications
## Switch Router
One of the primary applications of the SwitchBoard is to steer AT switch input to different devices as selected by the user. Current options are a 2x3 router where (2) switches (e.g., Sip and Puff/Bite) can be connected to one of three devices. A 1x6 router (one switch to six devices) is also available.
Device-to-Switch circuits are routed through the isolated relay contacts (and maybe the current sensor) only – no reading or retransmission of signals via the micro-controller is necessary. This largely eliminates any delay and concerns regarding voltage levels, grounding, or whatever signals a device might send through the switch.
## Mobility Device Controller
The five relays can facilitate communications with a mobility device controller, allowing movement in each direction.
## Notification / Alerting
Notifications and alerts received by a Feather can be conveyed to a user by activating a relay that turns on the appropriate indicator device(s).
# Configuration and Interfacing
## Addressing
Two address pads on the underside of the board ground the A1 and A0 address lines. The grounding trace between the pads can be cut to allow an address line to be pulled high. A short piece of wire can be soldered across the pads to reconnect the address lines to ground. Each SwitchBard should have a unique address when used with othe SwitchBoards on the same I2C bus.
A1	A0	Address
Grounded	Grounded	0
Grounded	Cut	1
Cut	Grounded	2
Cut	Cut	3

## Relay Interfacing
There is no external access to the relay set and reset coils. All switch contacts, NO, COM, NC x 10 are accessed via the through-hole solder points along the sides of the board. Labels are on the underside of the board. This isolates the device-to-switch circuit from the SwitchBoard and Feather electronics. Contact current should not exceed 2A.
Voltages above 24V (DC or rms AC) are strongly discouraged as this device is intended for low voltage use and no safety provisions have been made for high voltage use, nor have these boards been tested at significantly higher voltages. The potential for equipment damage and harmful electric shock to humans exists at higher voltages.
## Current Sensor Interfacing
The current sensor sensor measures the current between the V+ and V- terminals as the current goes through a 0.1 Ohm current shunt resistor.
Some models may include a GND terminal that allows the voltage and V+ and V- to be measured IF the source voltage references the same ground as the SwitchBoard. If a different ground is referenced, or the grounds are not co-located in the general vicinity of each other, DO NOT CONNECT THE GND terminal as ground loops may form and damage the SwitchBoard, Feather, and other equipment connected by means other than the relay contacts.
## GPIO Expander Pins
Unused I/O pins and the port interrupt pins are available at 2x4 header JP1.

INTA		INTB
GPA5		GPB5
GPA6		GPB6
GPA7		GPB7

## Power and I2C Lines
The 3.3VDC, Ground, SDA and SCL (I2C) lines are available at the 2x2 header.

SCL		SDA
3.3V		GND

# Components
## Relays
Kemet EE2-3TNUH-L
- Non-volatile, latching relay contacts (set & reset for NO and NC closure respectively).
- Double-pole, double-throw (DPDT, or two Form C) contacts where both poles operate in tandem to connect the common (CO) terminals to the normally open (NO) or normally closed (NC) contacts when set or reset respectively.
## GPIO Expander
Microchip MCP23017-E/SS
This is an I2C device that provides two general purpose bidirectional 8-bit I/O ports. Ten of these pins are used to trigger the relay drivers to turn on the set and reset coils of the five relays. The six remaining, unused pins, along with the port A and port B interrupt pins, are available for use and accessible at the 2x4 pin header.
## Relay Drivers
Texas Instruments ULN2003ANSR
These chips provides low-side switching of the relay coils via a Darlington pair transistor configuration. An integrated snubber or flyback diode to suppress inductive voltage transients when the coils are switched off.
## Current Sensor
Microchip INA-219AIDR
The INA219 is a high-side current shunt monitor. Current between the V+ and V- terminals is routed through a 0.1 Ohm resistor. The resistor voltage is sampled and the current computed (current = voltage / resistance) and reported back to the micro-controller on request.
Current should not exceed 3.1 amps (DC or AC rms). Voltages referenced to a common ground should be between -0.3 and +26 VDC.
## Reset Switch
A reset switch is provided that resets the GPIO Expander and the Feather board. The relays are not reset by the switch but may be reinitialized by Feather software.
## Power LED
A green LED indicates that the SwitchBoard FeatherWing has power (3.3V).
# Software
## Library
The SwitchBoard library is downloadable from
https://github.com/ATMakersOrg/ATMakers-SwitchBoard-Arduino-Library.

Class and key methods are:
Initialization:
class ATMakers_SwitchBoard
begin(curent_threshold_mA=1.0, address=0)
Manipulating the relay:
relaySet(relay_number 1-5)	Close the NO contacts, open the NC contacts.
relayReset(relay_number 1-5)	Close the NC contacts, open the NO contacts.
ResetAll()	Close the NC contacts, open the NO contacts for all relays.
Configuring the Current Sensor:
setCalibration_32V_2A()	Set max voltage at 32V, max current at 2A.
setCalibration_32V_1A()	Set max voltage at 32V, max current at 1A.
setCalibration_16V_400mA()	Set max voltage at 16V, max current at 400mA.
* The above methods set various registers in the INA219. Overflow will occur when the lower settings are exceeded. Damage to the shunt resistor and/or INA219 may occur if the upper settings are exceeded.

Testing & Reading Current Levels:
bool currentSensorActive(void)	Test if measured current is over the current threshold.
float currentThreshold(void)	Get the current value used in currentSensorActive().
float currentThreshold(new_threshold_mA)
Set the new current threshold, returns the old value.
float getCurrent_mA()	Get the measured current through the shunt resistor.

Reading Voltages at the Current Sensor:
float getSupplyVoltage_V()	Read the voltage at V+ (high side).
float getLoadVoltage_V()	Read the voltage at V- (low side).
float getShuntVoltage_mV()	Read the voltage across the shunt resistor.

Read Everything:
getCurrentSensorData(CS_Data&)	Read voltages, current, and current_active into the provided
CS_Data structure (by reference).

Accessing Extra I/O Pins on the GPIO Expander:
bool isExtraPin(pin 0-7)	Test if the pin is available for use.
pinMode(pin 0-7, direction INPUT|OUTPUT) Set the pin I/O mode.
digitalWrite(pin 0-7, level HIGH|LOW)	Set output level of OUTPUT pin.
pullUp( pin 0-7)	Turn on the internal pull-up for an INPUT pin.
int digitalRead(pin 0-7)	Read the level of an INPUT pin.
## Example Code
Example code is available at
https://github.com/ATMakersOrg/ATMakers-SwitchBoard-Arduino-Library/tree/master/examples

# Resources Used
## Voltage
## Current
## Timing
## Ratings

# Photographs & Diagrams
# Schematics for Switch Routers

GitHub & ATMakers.org links
Eagle files & Gerber config, zip files
# Board Revisions
## Rev B
Addresses a few issues in Rev A.
Mechanical:
- modified hole spacing for use with continuous headers (inserted holes between terminal blocks)
- adjusted row spacing for use with solderless breadboards (standard multiples of 0.1”).
Electrical:
- stronger pull-ups on the I2C lines for a sharper waveform and better noise tolerance
- reset line conditioning, added
  - a pull-up resistor,
  - a filter capacitor,
  - a current limiting resistor for when the reset line (and capacitor) is grounded.
- switched to a dimmer LED.
## Rev A (1.0)
Original release – first board run (& prototype).