ATMakers
SwitchBoard
Relay
FeatherWing
User's Guide

For Board Rev A (1.0) and B

Document DRAFT Version 1.0
2018-09-20

# Introduction
The ATMakers' SwitchBoard is a set of five relays and a current sensor arranged on a FeatherWing form factor PC board. An attached Feather micro-controller can control each of the five relays independently and read the current flowing through the current sensor terminals. A GPIO Expander facilitates the control of the relays via the I2C bus, thus freeing up any I/O pins that would be used otherwise.
The relays are double-pole, double-throw latching relays. Relay and current sensor I/O is available via solder terminals at the sides of the board where screw terminals, headers, or point-to-point wiring can be soldered.
Up to four SwitchBoards can be addressed on one I2C bus thereby allowing one Feather to control up to twenty DPDT latching relays.
The SwitchBoard concept was proposed by Bill Binko of ATMakers.org.
# Applications
## Switch Router
One of the primary applications of the SwitchBoard is to steer AT switch input to different devices as selected by the user. Current options are a 2x3 router where (2) switches (e.g., Sip and Puff/Bite) can be connected to one of three devices. A 1x6 router (one switch to six devices) is also available.
Device-to-Switch circuits are routed through the isolated relay contacts (and maybe the current sensor) only – no reading or retransmission of signals via the micro-controller is necessary. This largely eliminates any delay and concerns regarding voltage levels, grounding, or whatever signals a device might send through the switch.
## Mobility Device Controller
The five relays can facilitate communications with a mobility device controller, allowing movement in each direction.
## Notification / Alerting
Notifications and alerts received by a Feather can be conveyed to a user by activating a relay that turns on the appropriate indicator device(s).
# Configuration and Interfacing
## Addressing
Two address pads on the underside of the board ground the A1 and A0 address lines. The grounding trace between the pads can be cut to allow an address line to be pulled high. A short piece of wire can be soldered across the pads to reconnect the address lines to ground. Each SwitchBard should have a unique address when used with othe SwitchBoards on the same I2C bus.
A1	A0	Address
Grounded	Grounded	0
Grounded	Cut	1
Cut	Grounded	2
Cut	Cut	3

## Relay Interfacing
There is no external access to the relay set and reset coils. All switch contacts, NO, COM, NC x 10 are accessed via the through-hole solder points along the sides of the board. Labels are on the underside of the board. This isolates the device-to-switch circuit from the SwitchBoard and Feather electronics. Contact current should not exceed 2A.
Voltages above 24V (DC or rms AC) are strongly discouraged as this device is intended for low voltage use and no safety provisions have been made for high voltage use, nor have these boards been tested at significantly higher voltages. The potential for equipment damage and harmful electric shock to humans exists at higher voltages.
## Current Sensor Interfacing
The current sensor sensor measures the current between the V+ and V- terminals as the current goes through a 0.1 Ohm current shunt resistor.
Some models may include a GND terminal that allows the voltage and V+ and V- to be measured IF the source voltage references the same ground as the SwitchBoard. If a different ground is referenced, or the grounds are not co-located in the general vicinity of each other, DO NOT CONNECT THE GND terminal as ground loops may form and damage the SwitchBoard, Feather, and other equipment connected by means other than the relay contacts.
## GPIO Expander Pins
Unused I/O pins and the port interrupt pins are availbe at the 2x4 header.
## Power and I2C Lines
The 3.3VDC, Ground, SDA and SCL lines are available at the 2x2 header.
# Components
## Relays
Kemet EE2-3TNUH-L
- Non-volatile, latching relay contacts (set & reset for NO and NC closure respectively).
- Double-pole, double-throw (DPDT, or two Form C) contacts where both poles operate in tandem to connect the common (CO) terminals to the normally open (NO) or normally closed (NC) contacts when set or reset respectively.
## GPIO Expander
Microchip MCP23017-E/SS
This is an I2C device that provides two general purpose bidirectional 8-bit I/O ports. Ten of these pins are used to trigger the relay drivers to turn on the set and reset coils of the five relays. The six remaining, unused pins, along with the port A and port B interrupt pins, are available for use and accessible at the 2x4 pin header.
## Relay Drivers
Texas Instruments ULN2003ANSR
These chips provides low-side switching of the relay coils via a Darlington pair transistor configuration. An integrated snubber or flyback diode to suppress inductive voltage transients when the coils are switched off.
## Current Sensor
Microchip INA-219AIDR
The INA219 is a high-side current shunt monitor. Current between the V+ and V- terminals is routed through a 0.1 Ohm resistor. The resistor voltage is sampled and the current computed (current = voltage / resistance) and reported back to the micro-controller on request.
Current should not exceed 3.1 amps (DC or AC rms). Voltages referenced to a common ground should be between -0.3 and +26 VDC.
## Reset Switch
A reset switch is provided that resets the GPIO Expander and the Feather board. The relays are not reset by the switch but may be reinitialized by Feather software.
## Power LED
A green LED indicates that the SwitchBoard FeatherWing has power (3.3V).
# Software
## Library

## Examples
# Resources Used
## Voltage
## Current
## Ratings

# Photographs & Diagrams
# Schematics for Switch Routers

GitHub & ATMakers.org links
Eagle files & Gerber config, zip files
Board Revisions